## Slide 1: Inter-process Communications for Robotics Applications
Edward M. Roderick
Advisor: Dan Lofaro Ph.D

## Slide 2: Why Robotics Needs Inter-Process Communications (IPCs)
Provides a Modular System
Flexibility of connectivity
Scalable
Ideal for complex systems
Reduces impact of subsystem failure
  Increases safety in human proximity
  More robust robot
Eases robot limitations:
  Offloading computation
  Remote sensing
  Cloud databases
  Lighter/Smaller robot
Communication to other robots
Diversity of programming languages/styles

## Slide 3: Existing IPC Protocols
IPC | Local Communication | Network Communication
UDP (Sockets) | Y | Y
TCP (Sockets) | Y | Y
ZeroMQ (TCP Based) | Y | Y
ROS (TCP Based) | Y | Y
ACH (Shared Memory) | Y | N
Sockets: A library of IPC methods with the POSIX specification based on Internet and domain addresses[2].
Shared Memory: A fast local IPC method based on reading and writing to the same memory address. Susceptible to synchronization issues[2].
[2] N. Dantam and M. Stilman, “Robust and efficient communication for real-time multi-process robot software,” in Humanoid Robots (Humanoids), 2012 12th IEEE-RAS International Conference on, Nov 2012, pp. 316– 322.

## Slide 4: Sockets: TCP/UDP
Wireless control of mobile robots
Wireless controllers are common, as is Sockets
TCP retransmission causes delay time
UDP message limit 64 kbytes
Retransmission algorithm overcomes message losses
Assigned priority correlates to amount of retransmissions
[7] D. K. Cho, S. H. Chun, J. G. Ahn, Y. S. Kwon, J. H. Eom, and Y. I. Kim, “A udp-based protocol for mobile robot control over wireless internet,” in Robot Communication and Coordination, 2009. ROBOCOMM ’09. Second International Conference on, March 2009, pp. 1–4.
Figure 1: Network architecture for mobile robots[7].
Figure x: Retransmission algorithm at the base station (left) and mobile robot (right) [7].

## Slide 5: Sockets: ZeroMQ
Topology is the primary concept in ZMQ
Uses TCP as underlying transport
Abstracts networking layer. Messages sent to topology instead of IP addresses.
Several messaging patterns:
  Server/client
  Publish/Subscribe
  Request/Reply
Nodes can join and leave topologies dynamically
[9] M. Sstrik, “zmq: The theoretical foundation,” 250bpm, Tech. Rep., 09 2011.
ZeroMQ Theoretical Foundation
Figure 2: Example topologies of ZMQ messaging patterns. The flexibility of design is shown here [9].

## Slide 6: Sockets: ZeroMQ
Easy to implement; very similar to sockets
Scalable
Lock free code, avoids synchronization issues
Prevents priority inversion
Multiple threads communicate over ZMQ topologies
Wide array of available programming languages
Multithreading
[10] P. Hintjens and M. Sustrik, “Multithreaded magic with zmq,” iMatrix Corporation, Tech. Rep., 09 2010.
Example Code (python) [10]

## Slide 7: Shared Memory: ACH
Real-Time Multi-Process Robots
[2] N. Dantam and M. Stilman, “Robust and efficient communication for real-time multi-process robot software,” in Humanoid Robots (Humanoids), 2012 12th IEEE-RAS International Conference on, Nov 2012, pp. 316– 322.
Figure 3: Logical memory structure of ACH shared memory file
Low latency
Separate Data and index arrays allow for non head of line blocking
No data is lost when read or replaced, unlike sockets
Multiple readers and writers
Threadsafe via a mutex
Open source
Formally verified

## Slide 8: Shared Memory: ACH
Minimal latency is crucial for real time humanoid systems
Allows for proper priority inheritance
Prevents starvation
Publish/Subscribe or message bus interface
Muliple processes with varied priorities ensures critical processes run on time.
Figure 4: HUBO2 Platform[1]
Figure 5: Hubo2 Plus daemon communication flow chart[1].
Real-Time Multi-Process Robots / The ACH Library
[1] N. Dantam, D. Lofaro, A. Hereid, P. Oh, A. Ames, and M. Stilman, “The ach library: A new framework for real-time communication,” Robotics Automation Magazine, IEEE, vol. 22, no. 1, pp. 76–85, March 2015.
[4] M. Grey, N. Dantam, D. Lofaro, A. Bobick, M. Egerstedt, P. Oh, and M. Stilman, “Multi-process control software for hubo2 plus robot,” in Technologies for Practical Robot Applications (TePRA), 2013 IEEE International Conference on, April 2013, pp. 1–6.

## Slide 9: ROS
ROS cannot currently run on low level embedded systems.
Several interfaces exist for incorporating embedded systems.
Uses TCP as transport mechanism. Overhead can be detrimental to low powered systems.
Relies on communication links (Topics) and multiple processes (Nodes) to communicate between the core linux system and peripherals.
Must run a ROScore process that acts as intermediary between all nodes and topics. Can induce additional latency.
[3] P. Bouchier, “Embedded ros [ros topics],” Robotics Automation Magazine, IEEE, vol. 20, no. 2, pp. 17–19, June 2013.
Embedded Systems
Figure 6: ROS example network diagram [3].

## Slide 10: ROS
ROS excels at quickly incorporating off the shelf robots into large systems.
Large community with modular open source nodes reduces development time.
ROScore and heavy computation can be offloaded over computers defined in the ROSnetwork (TCP).
  Allows for cheaper, smaller and more power efficient robots.
  Ideal for educational systems
[12] A. Araujo, D. Portugal, M. Couceiro, and R. Rocha, “Integrating arduino-based educational mobile robots in ros,” in Autonomous Robot Systems (Robotica), 2013 13th International Conference on, April 2013, pp.
1–6.
Educational Platforms for ROS
Figure 7: Network topology example with multiple robots, sensors, and tele-operation devices. All off the shelf hardware.

## Slide 11: Typical System Layout
Modular design
Network communications
Integration of preexisting hardware
Choice software communication
Dealing with predetermined hardware communication
Figure 8: Typical layout of a robotic system

## Slide 12: Test Setup
Figure 9: Operational flow chart of test setup.
Figure 10: System diagram of test setup.
Single byte message
Test message eliminates handshaking from results[7].
10,000 samples
Millisecond accuracy of clock.
[7] D. K. Cho, S. H. Chun, J. G. Ahn, Y. S. Kwon, J. H. Eom, and Y. I. Kim, “A udp-based protocol for mobile robot control over wireless internet,” in Robot Communication and Coordination, 2009. ROBOCOMM ’09. Second International Conference on, March 2009, pp. 1–4.
Link 1: UDP, TCP, ZeroMQ, or ROS
Link 2: UDP, TCP, ZeroMQ, ROS, or ACH
Laptop, Raspberry Pi, OpenCM (Arduino)

## Slide 13: Test Results: Network Communication (Link 1)
Item | UDP | TCP | ZMQ | ROS
Average (ms) | 3.834 | 3.829 | 5.285 | 13.09
Min (ms) | 3.359 | 3.399 | 3.943 | 4.860
Max (ms) | 95.063 | 42.006 | 92.746 | 706.840
Std Deviation(ms) | 1.441 | .768 | 3.639 | 12.921
Figure 12: TCP (Link 1) and UDP (Link 2) Test Results
Figure 11: UDP (Link 1 and 2) Test Results - Control
Figure 13: ZMQ (Link 1) and UDP (Link 2) Test Results
Figure 14: ROS (Link 1 and Link 2) Test Results

## Slide 14: Test Results: Internal Communication (Link 2)
Item | UDP | TCP | ZMQ | ROS | ACH
Average (ms) | 3.834 | 4.774 | 5.000 | 17.571 | 3.752
Min (ms) | 3.359 | 4.079 | 3.853 | 5.680 | 3.219
Max (ms) | 95.063 | 43.974 | 161.833 | 709.943 | 73.533
Std Deviation(ms) | 1.441 | 1.160 | 3.171 | 9.958 | 1.705
Figure 16: UDP (Link 1) and ZeroMQ (Link 2) Test Results.
Figure 15: UDP (Link 1) and TCP (Link 2) Test Results
Figure 17: UDP (Link 1) and ROS (Link 2) Test Results
Figure 18: UDP (Link 1) and ACH (Link 2) Test Results
Note: Control Data (UDP links 1 and 2) not repeated

## Slide 15: Ideal System Design
Figure 19: Ideal robotic system favoring minimal latency
Figure 20: Ideal robotic system favoring data reliability

## Slide 16: References
[1] N. Dantam, D. Lofaro, A. Hereid, P. Oh, A. Ames, and M. Stilman, “The ach library: A new framework for real-time communication,” Robotics Automation Magazine, IEEE, vol. 22, no. 1, pp. 76–85, March 2015.
[2] N. Dantam and M. Stilman, “Robust and efficient communication for real-time multi-process robot software,” in Humanoid Robots (Humanoids), 2012 12th IEEE-RAS International Conference on, Nov 2012, pp. 316– 322.
[3] P. Bouchier, “Embedded ros [ros topics],” Robotics Automation Magazine, IEEE, vol. 20, no. 2, pp. 17–19, June 2013.
[4] M. Grey, N. Dantam, D. Lofaro, A. Bobick, M. Egerstedt, P. Oh, and M. Stilman, “Multi-process control software for hubo2 plus robot,” in Technologies for Practical Robot Applications (TePRA), 2013 IEEE International Conference on, April 2013, pp. 1–6.
[5] A. Shakhimardanov, N. Hochgeschwender, M. Reckhaus, and G. K. Kraetzschmar, “Analysis of software connectors in robotics,” in Intelligent Robots and Systems (IROS), 2011 IEEE/RSJ International Conference on, Sept 2011, pp. 1030–1035.
[6] J. Vella and S. Zammit, “Packet losses of multicast over 802.11n heterogeneous wireless local area network,” in Systems, Signals and Image Processing (IWSSIP), 2012 19th International Conference on,
April 2012, pp. 300–303.
[7] D. K. Cho, S. H. Chun, J. G. Ahn, Y. S. Kwon, J. H. Eom, and Y. I. Kim, “A udp-based protocol for mobile robot control over wireless internet,” in Robot Communication and Coordination, 2009. ROBOCOMM ’09. Second International Conference on, March 2009, pp. 1–4.
[8] A. Harris and J. Conrad, “Improving and designing sensors for the simulation environment for autonomous robots (sear),” in Southeastcon, 2013 Proceedings of IEEE, April 2013, pp. 1–5.
[9] M. Sstrik, “zmq: The theoretical foundation,” 250bpm, Tech. Rep., 09 2011.
[10] P. Hintjens and M. Sustrik, “Multithreaded magic with zmq,” iMatrix Corporation, Tech. Rep., 09 2010.
[11] S. Cousins, “Is ros good for robotics? [ros topics],” Robotics Automation Magazine, IEEE, vol. 19, no. 2, pp. 13–14, June 2012.
[12] A. Araujo, D. Portugal, M. Couceiro, and R. Rocha, “Integrating arduino-based educational mobile robots in ros,” in Autonomous Robot Systems (Robotica), 2013 13th International Conference on, April 2013, pp.
1–6.